## Slide 1
Report: Electricity Demand Forecasting with Hybrid Statistical and ML Algorithms
Data is the new oil. Insight is the new currency. Models become new electricity.
STAT303: Time Series Analysis
Authors: Tatiana Gonzalez Grandon, Johannes Schwenzer, Thomas Steens, Julia Breuing
Professor Dr. Sithu Aung

## Slide 2
PAPER OVERVIEW
  Predict national electricity demand (hourly, long-term) for Ukraine
Grounded in evidence, not guesswork
Reduce the unnecessary costs
Improved Decision-Making
Cost Reduction
Monitor and improve the electricity load continuously
Performance Optimization
STAT303: Time Series Analysis

## Slide 3
Introduction
Conclusion
About
Home
  Electricity drives economic growth and development, today.
  Key role in low - carbon transition
  Forecast accuracy → major cost savings (e.g., 1% = millions saved)
  Forecasting demand is still difficult.
  The system is complex, influenced by many factors
  Requires predictions across different time horizons (from daily operations to long-term planning)
Limitations
STAT303: Time Series Analysis

## Slide 4
About
Home
Types of Forecasting
To handle this, forecasting is divided into three levels:
For daily operations
Short-term
For planning and maintenance
Medium-term
For infrastructure and investment
Long-term
Context
STAT303: Time Series Analysis

## Slide 5
Literature Review
Hybrid Models (Key Idea)
  Combine CST + ML
  Hybrid CST + LSTM model
  Predict long-term demand with hourly detail
  Case study: Ukraine (2013–2020)
This Paper will contribute:
About
Home
Two Main Approaches
  Classical Statistical Techniques (CST)
    Regression, ARIMA (Linear model)
  Machine Learning (ML)
    ANN, RNN, LSTM (Non-linearity)
Literature on electricity load forecasting
  CST: MAPE ~2.6%–3.9%
  ML: MAPE ~3.6%–3.7%
  Mixed results → no clear winner
Performance Insights (Past papers)
  ML mostly used for short-term forecasting
  Long-term forecasting still underdeveloped
  Models often tested separately
Limitations/Gap in Literature
Context
STAT303: Time Series Analysis

## Slide 6
Overview of Ukraine’s Electricity Demand
  Developing country in political & economic crisis
  Energy security is critical
Ukraine’s Context
01
  Demand affected by macroeconomic factors:
      Population, GDP, GDP growth
  Major drops:
      2009 financial crisis
      2014 Crimean crisis
02
Long-Term Trends
  Winter → highest electricity demand
  Daily (hourly) peaks exist
  Mid-term + short-term patterns visible
Seasonal Patterns
03
Electricity demand is strongly influenced by temperature in a nonlinear “hockey-stick” pattern, with much higher usage in cold weather, since heating (5.3%) has a greater impact than cooling (1.9%).
Context
About
Home
  Strong influence on demand
  Nonlinear relationship (not straight line)
  “Hockey stick” pattern:
    Very high demand in cold weather
    Moderate increase in hot weather
04
Temperature Effect
STAT303: Time Series Analysis

## Slide 7
Home
Model Structure
  Electricity demand is split into 3 components:
      Long-term (yearly trend)
      Medium-term (daily/seasonal)
      Short-term (hourly variation)
  Additive model: combines all components
  Tested 2¹⁸ regression models
  Ranked using AICc
  5-fold cross-validation
  Filtered using RMSE and MAE
Model Selection Process
  Predict yearly average demand
  Based on macroeconomic factors
      GDP deflator
      Industrial value added
      GDP growth rate
      Service sector contribution
  Uses multiple linear regression
      D̄L(y) = βL,1 + βL,2 * GDPδ(y) + βL,3 * IND(y) + βL,4 * GRO(y) + βL,5 * SERV(y) + w(y)
Long-Term Model
  Residuals tested for normality (Shapiro-Wilk)
  p-value = 0.62 → good fit
  Variance of noise estimated
Model Validation
Macroeconomic factors strongly explain long-term electricity demand. Model is statistically valid and stable
Models
Results
STAT303: Time Series Analysis

## Slide 8
Mid-Term Model
First, modeled using a linear regression (LM) with
      Temperature,
      Seasonality,
      Holidays, and
      Lag effects
Remaining errors (residuals) still contain structure → Modeled separately
Results
Models
Home
Two approaches are used for residuals:
  ARIMA(30,1,25) → captures linear autocorrelation patterns
  LSTM (Seq2Seq + attention) → captures nonlinear and long-term dependencies
  Final step combines both into a hybrid model
STAT303: Time Series Analysis

## Slide 9
Results
Models
Home
Hybrid Model Results
LSTM-based hybrid model gives the best forecasting accuracy
  LM
  LM + ARIMA
  LM + LSTM ✅
  LM + ARIMA + LSTM
Tested combinations:
We first model the main trend using regression, then improve accuracy by modeling residuals using ARIMA and LSTM
STAT303: Time Series Analysis

## Slide 10
Results
Models
Home
  Linear regression:
    Hour-of-day (ToH) dummy variables
    Separate models for each month & weekday
  Residual modeling:
    ARMA models (stationary data)
    Captures short-term dependencies
    Works well due to strong daily cycles
Model Structure
  Hourly demand is highly repetitive
  Simple models (Regression + ARMA) are enough
  No need for complex ML like LSTM
Model Analytics
Short-Term Model
  Focus: hourly demand variation within a day
  Remove long + medium effects → isolate daily pattern
Hourly Patterns
STAT303: Time Series Analysis

## Slide 11
Results
Models
Home
Finalized Model
  Test on real data
  Train model: 2013–2018
  Test model: 2019 & 2020
Checks if the model works on unseen data
  Long-term (yearly trend)
  Medium-term (daily + seasonal)
  Short-term (hourly pattern)
Combine all models
  MAPE ≈ 3.17% (very accurate)
  2019: 2.79%
  2020: 3.56%
Results
STAT303: Time Series Analysis

## Slide 12
Conclusion
This paper proposes a hybrid model for national electricity demand forecasting that combines classical statistical methods with machine learning.
Conclusion
About
Home
Long-term is modeled using regression on macroeconomic factors
Medium-term uses regression + ARIMA + LSTM
a.
b.
Short-term uses regression + ARMA
c.
The model splits demand into
The model performs well (~3% error), but it depends on future macroeconomic and weather data. The hybrid model balances interpretability and accuracy, providing reliable long-term electricity forecasts while capturing complex real-world patterns.

## Slide 13
Requires future macroeconomic data
Depends on weather projections
Limitation:
Conclusion
About
Home
Future Work
  Apply to other countries (Myanmar)
  Fully automated forecasting system
STAT303: Time Series Analysis

## Slide 14
Thank You
For Your Attention
Data is not about numbers, it's about understanding
Conclusion
About
Home
Special Thanks to Prof. Sithu Aung for your guidance and support throughout the course
STAT303: Time Series Analysis

## Slide 15
References
  Grandon, T. G., Schwenzer, J., Steens, T., & Breuing, J. (2023, April 11). Electricity Demand Forecasting with Hybrid Statistical and Machine Learning Algorithms: Case Study of Ukraine. arXiv.org. https://arxiv.org/abs/2304.05174
  Huang, C., & Petukhina, A. (2022). Applied Time Series Analysis and Forecasting with Python. In Statisctics and computing/Statistics and computing. https://doi.org/10.1007/978-3-031-13584-2
STAT303: Time Series Analysis